Vibration deoiler

Operation Instruction

- Thank you for choosing machines from Jinan Zhuoheng Extrusion Machinery Co., Ltd.

- please read this operation instruction before using the machine

- Welcome to inquiry if anything unclear

Jinan Zhuoheng Extrusion Machinery Co., Ltd

I Ovewview

Vibration conveyor is one of the special equipment used in puffed snack food processing line for conveying materials. Relying on high frequency vibration made by vibration motor eccentric vibration, make the material vibration sliding in the vibrating screen,durign the period of conveying, screen away powder mixed in the materials. Saves time and effort, safe and reliable.

II Vibration Conveyor Structure

III  Main Technical Data

1. Dimension( L*W*H) 1870×600×750mm

2. Voltage: 380V, 50 Hz

3. Motor Power: 0.37 k w

4 Capacity: 150-200kg/h

Iv Installation and Maintenance

1 According to the configuration, put vibration conveyor on hard and flat ground. Generally, connect Joint hopper of vibration conveyor with the Rotary cut cover of the extruder, while connect the outlet of the vibration conveyor with the feeding material hopper of air conveyor of hoister.

2 Connect the vibration conveyor’s power line to main power supply control plate correctly.

3 Turn on air switch of vibration conveyor, adjust the amplitude of vibration motor, to make it meet the production requirements

4 In the course of work, pay attention to safe operation. When the machine stops working, must do the cleaning.

5 When operating the machine, should be in strict accordance with the manual operation, and do maintenance on time.

Matters need attention

1when the machine starts to work, should check whether the amplitude could meet production requirements.

2 when cleaning materials inside screen body, you must cut off the power supply firstly; when the machine stop working then starts cleaning.

3 In case of power failure and such emergency, when the machine stops working, should clean up the material in screen body timely.

4 Regular check the circuit line, prevent from getting an electric shock loose, insulation aging circuit fault.

5 Must pay attention to production safety

The Editor:

Thank you for choose the Jinan Zhuoheng Extrusion Machinery; if you company increase product variety or enlarge the production, our company also have other types of equipments for your select. (reference list). Our company adhering to the "excellent quality, long-last reputation" of the enterprise purpose and "mutual cooperation and common development" business philosophy, Our adhere to the principle of “Sincerity, Innovation and excellence” spirit and dedication, we provide you the good serve and supply on-site installation, commissioning service and free training operators and free offer advanced technology formula and ensure the long-term supply spare parts, the warranty of the machine is for one year free. If there are some problems when need to consult or purchase the spare parts or special order, you can feel free to contact with us, we will meet your requirements as soon as possible.

Thanks again for your using Zhuoheng Extrusion Machinery, Zhuoheng service can bring your convenience and satisfaction, wish have a thriving business and sincerely hope you can propose the ideas and suggestions.