GTW-D Single drumflavoring line

Operation Instructions

- Thank you for choosing machines from Jinan Zhuoheng Extrusion Machinery Co., Ltd.

- please read this operation instruction before using the machine

- Welcome to inquiry if anything unclear

Jinan Zhuoheng Extrusion Machinery Co., Ltd

Ovewview

Single roller flavoring line including advice seasoning machine, single drum mixing machine and oil- spraying machine three parts. Material through ascension machine into the drum, do oil injection inside the drum,to make the material surface uniform coating a layer of oil film; At the same time start the spraying condiment in the seasoning machine, through the rotation of the roller and mixing of the material dia cone, to make the condiment uniform adhesive in the surface of the product, in order to make the products taste required.

I hoister

1. Dimension( L*W*H) 2618×600×1638mm

2. Voltage: 220V-380v, 50 Hz

3. Motor: 0.37+0.2kw

4. Capacity: 150-200kg/h

II Single drum flavoring machine

1. Dimension( L*W*H)2828×750×1468mm

2. Voltage: 380v, 50 Hz

3. Motor: 0.75kw

4. Capacity: 150-300kg/h

III oil-spaying machine

1. Dimension( L*W*H) 980×600×780mm

2. Voltage: 220-380v

3. Motor: 0.37kw

4. Capacity: 150-300kg/h

Iv Installation and Maintenance

1. According to the sequence of hoist – oil-spraying machine - single drum seasoning machine, lay them on the hard place and flat ground.  Connect hoisting machine with the equipment in the production line in front and makethe hopper of the hoister stretch to barrel inside of single roller seasoning machine;

2. According to the length of oil spraying pipe to determine the placement of spraying machine, and take sprinkler spray tubing fixed in installed hoop card, with oil  injection nozzle end into the drum in about 450 mm, nozzle spray Angle is 45 ° inclined Angle;

3. Set oil heating temperature of the oil spraying machine for 55 ℃ - 65 ℃, add oil then cover the oil storage barrel cover;When begin to work, control the pump speed, to control the quantity of oil injection.

4 Add the seasoning in external condiment hopper inside, during production, control the speed of seasoning feed screw, to adjust the amount of the condiment that added.

5 Start single roller seasoning machine, when the material into the hoist drum start sparying machine to do oil injection, open the seasoning feed system, according to the product requirements to adjust injection quantity and amount of outside seasoning.

6 When operating the machine, please be strictly according to the operation instruction, and do the maintenance on time.

Matters need attention

1 All the equipments must be ground fault protection

2 Set production temperature, should be according to intelligent temperature control meter specification.

3. In case of power failure and such emergency, when the machine stops working, clean up the material out from barrel manually in time.

4 Regular checks the circuit line, prevent from getting an electric shock loose, insulation aging circuit fault.

5Must pay attention to production safety

The Editor:

Thank you for choose the Jinan Zhuoheng Extrusion Machinery; if you company increase product variety or enlarge the production, our company also have other types of equipments for your select. (Reference list). Our company adhering to the "excellent quality, long-last reputation" of the enterprise purpose and "mutual cooperation and common development" business philosophy, Our adhere to the principle of “Sincerity, Innovation and excellence” spirit and dedication, we provide you the good serve and supply on-site installation, commissioning service and free training operators and free offer advanced technology formula and ensure the long-term supply spare parts, the warranty of the machine is for one year free. If there are some problems when need to consult or purchase the spare parts or special order, you can feel free to contact with us, we will meet your requirements as soon as possible.

Thanks again for your using Zhuoheng Extrusion Machinery, Zhuoheng service can bring your convenience and satisfaction, wish have a thriving business and sincerely hope you can propose the ideas and suggestions.